## Slide 1
Asynchronous Data Transfer
Lecture 43-45

## Slide 2
Data Transfer
Asynchronous data transfer between two independent units requires that
control signals be transmitted between the communicating units to
indicate the time at which data is being transmitted
Synchronous and Asynchronous Operations
Synchronous - All devices derive the timing information from common clock line
Asynchronous - No common clock
Asynchronous Data Transfer

## Slide 3
Asynchronous data transfer enables computers to send and receive data without having to wait for a real-time response. With this technique, data is conveyed in discrete units known as packets that may be handled separately.
Terminologies used in Asynchronous Data Transfer
Sender: The machine or gadget that transfers the data.
Receiver: A device or computer that receives data.
Packet: A discrete unit of transmitted and received data.
Buffer: A short-term location for storing incoming or departing data.
Classification of Asynchronous Data Transfer
Strobe Control Method
Handshaking Method
Asynchronous Data Transfer

## Slide 6
Asynchronous Data Transfer
Strobe pulse
- A strobe pulse is supplied by one unit to indicate the other unit when the transfer has to occur
Two Asynchronous Data Transfer Methods
Handshaking
- A control signal is accompanied with each data being transmitted to indicate the presence of data
- The receiving unit responds with another control signal to acknowledge receipt of the data

## Slide 7
* Employs a single control line to time each transfer
* The strobe may be activated by either the source or the destination unit
Strobe Control

## Slide 8
Strobe Control

## Slide 9
Handshaking
Strobe Methods
Source-Initiated
The source unit that initiates the transfer has no way of knowing whether the destination unit has actually received data
Destination-Initiated
The destination unit that initiates the transfer no way of knowing whether the source has actually placed the data on the bus
To solve this problem, the HANDSHAKE method introduces a second control signal to provide a Reply to the unit that initiates the transfer

## Slide 10
Source Initiated Transfer using Handshaking
* Allows arbitrary delays from one state to the next
* Permits each unit to respond at its own data transfer rate
* The rate of transfer is determined by the slower unit
Block Diagram
Timing Diagram
Accept data from bus.
Enable data accepted
Disable data accepted.
Ready to accept data
(initial state).
Sequence of Events
Place data on bus.
Enable data valid.
Source unit
Destination unit
Disable data valid.
Invalidate data on bus.
Source
unit
Destination
unit
Data accepted
Data bus
Data valid
Valid data
Data valid
Data accepted

## Slide 11
Destination Initiated Transfer
using Handshaking
* Handshaking provides a high degree of flexibility and reliability because the successful completion of a data transfer relies on active participation by both units
* If one unit is faulty, data transfer will not be completed -> Can be detected by means of a timeout mechanism
Block Diagram
Source
unit
Destination
unit
Ready for data
Data valid
Sequence of Events
Place data on bus.
Enable data valid.
Source unit
Destination unit
Ready to accept data.
Enable ready for data.
Disable data valid.
Invalidate data on bus
(initial state).
Accept data from bus.
Disable ready for data.
Ready for data
Data valid
Data bus
Valid data

## Slide 12
Serial Transfer
Asynchronous serial transfer
Synchronous serial transfer
Asynchronous parallel transfer
Synchronous parallel transfer
- Employs special bits which are inserted at both ends of the character code
- Each character consists of three parts; Start bit; Data bits; Stop bits.
A character can be detected by the receiver from the knowledge of 4 rules;
- When data are not being sent, the line is kept in the 1-state (idle state)
- The initiation of a character transmission is detected by a Start Bit , which is always a 0
- The character bits always follow the Start Bit
- After the last character , a Stop Bit is detected when the line returns to the 1-state for at least 1 bit time
The receiver knows in advance the transfer rate of the bits and the number of information bits to expect
Four Different Types of Transfer
Start
Stop
bits
Character bits
1
1
0
0
0
1
0
1
Asynchronous Serial Transfer

## Slide 13
Chip select
I/O read
I/O write
CS
RS
RD
WR
Timing
and
Control
Bus
buffers
Bidirectional
data bus
Transmitter
register
Control
register
Status
register
Receiver
register
Shift
register
Transmitter
control
and clock
Receiver
control
and clock
Shift
register
Transmit
data
Transmitter
clock
Receiver
clock
Receive
data
CS RS Oper. Register selected
0 x x None
1 0 WR Transmitter register
1 1 WR Control register
1 0 RD Receiver register
1 1 RD Status register
Internal Bus
A typical asynchronous communication interface available as an IC
Universal Asynchronous
Receiver Transmitter

## Slide 14
Universal Asynchronous
Receiver Transmitter
Transmitter Register
- Accepts a data byte(from CPU) through the data bus
- Transferred to a shift register for serial transmission
Receiver
- Receives serial information into another shift register
- Complete data byte is sent to the receiver register
Status Register Bits
- Used for I/O flags and for recording errors
Control Register Bits
- Define baud rate, no. of bits in each character, whether to generate and check parity, and no. of stop bits

## Slide 15
First In First Out Buffer
* Input data and output data at two different rates
* Output data are always in the same order in which the data entered the buffer.
* Useful in some applications when data is transferred asynchronously
4 x 4 FIFO Buffer (4 4-bit registers Ri),
4 Control Registers(flip-flops Fi, associated with each Ri)
The figure is shown for reference in next slide

## Slide 16
4-bit
register
S
R
F
F'
1
1
4-bit
register
S
R
F
F'
2
2
4-bit
register
S
R
F
F'
3
3
4-bit
register
S
R
F
F'
4
4
F
F
S
R
F
F'
S
R
Clock
Clock
Clock
Clock
Data
output
Output
ready
Delete
Data
input
Insert
Input ready
Master clear
R1
R2
R3
R4

## Slide 17
Modes of Transfer – Programmed I/O
3 different Data Transfer Modes between the central
computer(CPU or Memory) and peripherals;
Program-Controlled I/O
Interrupt-Initiated I/O
Direct Memory Access (DMA)
Data transfer from I/O device to CPU
Program-Controlled I/O:
- Result of I/O Instructions written in Computer Program.
Each data item transfer is initiated by an instruction in the program.
CPU stays in program loop until the I/O indicates that it is ready for the data transfer, so it is
time consuming.

## Slide 18
Inter Processor Arbitration
System Bus - A Backplane level bus
- Printed Circuit Board
- Connects CPU, IOP, and Memory
- Each of CPU, IOP, and Memory board can be plugged into a slot in the system bus
- Bus signals are grouped into 3 groups
Data, Address, and Control(plus power)
- Only one of CPU, IOP, and Memory can be granted to use the bus at a time
- Arbitration mechanism is needed to handle multiple requests
e.g. IEEE standard 796 bus
- 86 lines
Data: 16(multiple of 8)
Address: 24
Control: 26
Power: 20

## Slide 19
Synchronous and Asynchronous
Data Transfer
Synchronous Bus
Each data item is transferred over a time slice known to both source and destination unit
- Common clock source Or, separate clock and synchronization signal is transmitted periodically to synchronize the clocks in the system
Asynchronous Bus
Each data item is transferred by Handshake mechanism
- Unit that transmits the data transmits a control signal that indicates the presence of data
- Unit that receiving the data responds with another control signal to acknowledge the receipt of the data
Strobe pulse - supplied by one of the units to indicate to the other unit when the data transfer has to occur

## Slide 20
During an asynchronous data transfer, two devices manage their communication using handshaking. It is guaranteed that the transmitting and receiving devices are prepared to send and receive data. Handshakes are essential in asynchronous communication since there is no clock signal to synchronize the data transfer.
During handshaking, we use two types of signals mostly they are request-to-send (RTS) and clear-to-send (CTS). The receiving device is notified by an RTS signal when the transmitting equipment is ready to provide data. The receiving device responds with a CTS signal when it is ready to accept data.
once data is transmitted to the receiver end. the receiver generates a signal that it has done by sending an acknowledgment (ACK) signal. If the data is not successfully received, the receiving device will notify that a new transmission is necessary via a negative acknowledgment (NAK) signal.
Handshaking Method For Data Transfer

## Slide 21
The handshaking procedure guarantees synchronized and dependable data delivery. Additionally, it allows for flow management, preventing the transmitting device from sending the receiving device an excessive amount of data all at once. In order to offer flow control, handshaking signals are utilized to regulate the rate at which data is sent.
The Handshaking Method in asynchronous data transfer is used in different devices for the transfer of data to ensure reliable communication.

## Slide 22
IEEE Standard 796 Multibus Signals
Bus signal allocation
- address
- data
- control
- arbitration
- interrupt
- timing
- power, ground